## Slide 1
TENDO Hydraulic expansion technology
Quality and precision with over 35 years of experience

## Slide 2: Content
Overview
TENDO
Application examples
Milling test

## Slide 3: Content
TENDO
Application examples
Milling test
Overview

## Slide 4
Up to any chipping

## Slide 5: Product overview

## Slide 6: Product overview
TENDO Hydraulic expansion technology

## Slide 7: Content
Application examples
Milling test
Overview
TENDO

## Slide 8: TENDO

## Slide 9
Notes: Actuation screw
Clamping element
Seal
Expansion sleeve
Chamber system
base body
Length-setting screw
Tool shank

## Slide 10: TENDO Principle of function

## Slide 11: Technical highlights
The set-up time killer! Precise tool change without peripheral equipment
μ-accurate tool change in seconds
Simple handles for changing the tool quickly and reliably
Insert the tool into the hydraulic expansion technology, screw in the clamping screw with an allen key to the back stop turn in – ready
The clamping results: highest run-out accuracy
Convincingly simple handling with the allen key
No additional capital expenditure for peripheral equipment
Downtimes and set-up times at the machine are reduced
Maintenance costs or failure of external clamping devices are no longer applicable

## Slide 12: Features
Run-out and repeat accuracy
Optimal continous run-out and repeat accuracy of < 0.003 mm
Even cutting actions
Minimizes wear to the cutting edges of the tool
Increases tool service life considerably
Reduces the costs incurred for regrinding or buying new tools

## Slide 13: Features
Excellent vibration damping for perfect surfaces
The hydraulic sytem is synonymous with excellent vibration damping
Micro-blowouts on the cutting edge of the tool are prevented
Achieves optimum workpiece surfaces
The spindle performance will be enhanced
The tool service life is considerably increased and costs reduced

## Slide 14: Features
High flexibility through the use of intermediate sleeves
Application of slotted or coolant-proof intermediate sleeves
Different tool diameters ranging from 0.8 – 25 mm tensible
Can be used flexibly within the clamping range
The run-out accuracy of the sleeve is < 0.003 mm

## Slide 15: Features
Dirt resistance for long lasting functional reliability
Completely closed TENDO system
Prevents the penetration of dirt, chips, coolants, and grease
Clamping range is not damaged
Functionality and perfect tool clamping system remain fully preserved
Freedom from maintenance and a long service life for the TENDO clamping system are guaranteed

## Slide 16: Features
Dirt grooves for reliable torque transmission
Enormous clmaping pressure
Displacement of oil, grease, or grease residue into the dirt groove
The clamping face remains dry
Reliable torque transmission is guaranteed

## Slide 17: Features
All commercially available shank types can be clamped for process reliable clamping
Tools with both smooth cylindrical shanks in accordance with DIN 6535, Type HA up to Ø 32 mm and also those with recesses in accordance with:
DIN 1835 Types B, E DIN 6535 Types HA, HB, HE can be clamped directly and without the use of an intermediate sleeve

## Slide 18: TENDO E compact

## Slide 19: The TENDO-E compact
TENDO General:
Run-out accuracy 0.003 mm
Excellent vibration damping
 protects tools
 Better quality of workpieces
Tool change by hand in seconds
Identical torques at any clamping
TENDO-E compact
900 Nm at ø20 / 2000Nm at Ø32

## Slide 20: TENDO-E compact Ø 32 mm: max. continuous torque over 2000 Nm!!!

## Slide 21: TENDO E compact
High radial rigidity for the best shape accuracy
Optimal radial rigidity through a sturdy base body prevents lateral deflection during the cutting process
Your benefit: high part accuracy geometry at the workpiece combined eith the highest removal rates (e. g. 400 cm³/min for 42CrMo4*)
High torque up to 900 Nm (Ø 20) for maximum volume machining
Compact design
Strong holding forces
Thus high torque transmission
Your benefit: a significantly higher metal cutting volume
* depending on machine tool and tool

## Slide 22: TENDO E compact
Shorter processing times. Faster amortization.

## Slide 23: TENDO E compact
The 7 bull's eye with TENDO E compact:
1:0 The torque monster - Up to 60 % greater torques
than commercially available hydraulic expansion toolholders.
(For Ø 16 up to 700 Nm with dry, up to 350 Nm with oily tool shank).
2:0 The precision guarantor - More than 70 % better run-out than ER collet chucks
3:0 The endurance runner - Up to 40% more volume metal removal possible,
before the tool has to be reground.
BT 30* Ø 12 and Ø 20
*Coolant supply as per DIN 69871 AD

## Slide 24: TENDO E compact
The 7 bull's eye with TENDO E compact:
4:0 The more intelligent - Up to 40% longer service life due to oil shock absorber effect.
5:0 Ingeniously simple - ingeniously efficient! Up to 80 % faster tool change.
6:0 The price miracle - Up to 65 % procurement cost savings!
7:0 The perfectionist - Almost 100 % reproducible tool change <0.003mm.
BT 30* Ø 12 and Ø 20
*Coolant supply as per DIN 69871 AD

## Slide 25: TENDOzero

## Slide 26: TENDOzero
μ-accurate! To 0.000 mm in the twinkling of an eye
Professional for tight tolerances in drilling, reaming and spindling, where perfect concentricity is required.
Minimal concentricity errors of the tool, the holder and the machine spindle can be compensated individually
Permanent concentricity adjustable to 0.000 mm for optimum form and position tolerances
Perfect vibration damping for up to 50 % longer tool life
Easy handling for the exact adjustment of high-quality precision tools

## Slide 27: TENDOzero
  A TORX PLUS® key is used on the four set-screws to correct the angular position of the clamped precision tool, and the run-out accuracy is set to 0.000 mm

## Slide 28: TENDO ES

## Slide 29: TENDO ES
Space-saving! Precision in tight machine rooms
With zero interfering contour
Is used when every centimeter in the machine room counts
Extremely short hydraulic expansion toolholder
Perfectly suited for machining large workpieces – even when space in the machine room is tight – and for deep-hole drilling
Tools are mounted directly in the mounting taper
The mounting taper is supported in the spindle
Result: Maximum radial rigidity at high torques and plenty of additional space in the machine room

## Slide 30: TENDO ES
Ideal for deep-hole drilling:
Extremely short design
Frees up plenty of machine room space
Guarantees that there is sufficient freedom of movement for the axes before tool immersion
Collisions are eliminated

## Slide 31: TENDO SDF-KSR
Notes: Drive worm (set screw)
Clamping actuation
Drive worm (adjustment screw)

## Slide 32: TENDO SDF-KSR
More precise! Radial length adjustment for micron precise positioning
When the sensitive adjusting mechanism is oriented, this set-up time minimizer gives you micron precise positioning for the tool length
Length-setting screw equipped with a front and back stop, self-locking, 10 mm adjustment travel for all clamping diameters
Position of the tool can′t be changed by its own weight or through axial pressure
The balancing grade is not affected
Radial length adjustment can be actuated easily and process reliably using a set screw and an Allen key
Micron precise length adjustment of the machining tools using the compact adjusting mechanism

## Slide 33: TENDO SDF-KSR
  Possible applications, e. g. on multi-spindle machines
  Radially operated adjustment mechanism for pre-setting the tool length with micron accuracy in seconds

## Slide 34: TENDOturn

## Slide 35: TENDOturn
Low-vibration! Improvement of surface finish by up to 300%
Applications on lathes/milling centers
Versatile clamping range by virtue of intermediate sleeves
Run-out and repeat accuracy of < 0.003 mm (DSE double clamping insert)
Easy handling
Unique vibration damping
This helps to realize excellent workpiece surfaces
Axial length-setting screw
All shank types can be clamped, including Weldon and Whistle Notch
Improvement of vibration damping
Visible improvement in the surface quality by up to 300%

## Slide 36: TENDOturn
TENDOturn lathe clamping insert DKE
Increase the productivity by using the lathe clamping insert DKE
Does not require any specific interface
Can be held in any customary VDI bore rod holders in order to absorb vibrations
TENDOturn double clamping insert DSE
Modular insert for driven tools, for perfect performance on existing equipment
Maximum run-out quality and great vibration damping ensure optimum results
Uniform internal/external clamping force centers the insert providing maximum holding forces correct and precise clamping of your tool

## Slide 37: TENDO WZS for tool grinding

## Slide 38: TENDO WZS for tool grinding
Process reliable! Through maximum run-out accuracy < 0.003 mm
Uncompromisingly meets the high demands in tool sharpening
High run-out and repeat accuracy
Material is removed evenly during the grinding procedure
Increases the process reliability for grinding and sharpening operations
Enables you to clamp shank tools up to 32 mm in diameter as well as special tools with large shank lengths of up to 95 mm depth
Intermediate sleeves enhance the clamping options
Especially slim interfering contour for improved interference between grinding wheel
Optimal shape accuracy, surface quality, and run-out accuracy of the cutting edges of the tool ensures better chip flow and a more even cutting action
Versatile clamping range due to intermediate sleeves

## Slide 39: TENDO WZS for tool grinding
  With ist 25° chuck chamfer, TENDO WZS has an optimally adapted interfering contour for the tool grinding process in comparison to other hydraulic toolholders

## Slide 40: TENDO SVL

## Slide 41: TENDO SVL
Superior! Long, slim design, and optimized interfering contours
Predestined and designed for the precise machining of hard-to-reach areas
Is setting the standards in regard to set-up time and costs
The extension can be quickly clamped in every type of precision tool-holder
Huge advantage: a single TENDO extension can be fitted with a variety of standard tools, dispensing with the need for expensive special tools
Clamping in seconds without peripheral equipment
Proven hydraulic expansion technology
Excellent vibration damping
Suitable for nearly every precision toolholder, commercially available shank types can be clamped
Option to use intermediate sleeves

## Slide 42: TENDO SVL
TENDO SVL extensions fit in almost all toolholding systems

## Slide 43: TENDO SVL
  Optimized interfering contour
  Ideal for bores on deep parts in fixture cosntruction
  Micron precise tool changes in seconds guaranteed – even in the machine
  Clamping screw actuated to a dead stop using an Allen key, and the tool is clamped

## Slide 44: Content
Milling test
Overview
TENDO
Application examples

## Slide 45: SCHUNK & DMG

## Slide 46: The TENDO-EC

## Slide 47: Applications
Milling operation in tool making Milling of die inserts

## Slide 48: Applications
High-speed milling of a copper electr ode HSC hard milling of a for ging die

## Slide 49: Applications
  Prefinishing of base jaws
  TENDO with radial length adjustment on double spindle
  Machining a piston bore with PKD reamer
  Combination TENDO + TRIBOS SVL extension

## Slide 50: Applications
High-performance drilling in machine building Profile cutting in mould making

## Slide 51: Content
Overview
TENDO
Application examples
Milling test

## Slide 52: Milling test TENDO vs. CELSIO
Click me!

## Slide 53: Milling test TENDO vs. CELSIO

## Slide 54: Milling test TENDO vs. CELSIO